Vital Signs EQUIPMENT DAY
Sketch Exercise No. 2

High and Low SURFACE TEMPERATURES

(Raytek portable pyrameter)

Your instrument of choice for this exercise is the Raytek Ranger portable infrared pyrameter - a device for measuring surface temperatures.  This pyrameter concentrates and measures the longwave infrared radiation emitted by a surface.  It then calculates the temperature of the emitting surface using a fixed emissivity value supplied by the user. It has a nifty integrated laser pointer to indicate the surface position being measured.

Your challenge:

Find the hottest and coldest surfaces possible within a 12-minute survey of Lawrence Hall.

Do this:

1. Verify that the Raytek Ranger has an emissivity setting of 0.95.

2. Take measurements of the surfaces you believe will be relatively hot or cold. To take a reading just pull the trigger to turn on the laser, align it with your target, and read the surface temperature from the instrument’s display.

3. Note the location and value of your extreme readings in the spaces provided below.

Coldest reading:

Location of coldest reading:

Hottest reading:

Location of hottest reading: