Vital Signs EQUIPMENT DAY
Sketch Exercise No. 8

Is there GLARE in this room?

(Minolta Luminance Meter)

The quality of lighting may be described in terms of luminances (brightness), diffusion, uniformity, and chromaticity of the lighting. Excessive luminance (luminance ratios) in the field of vision is commonly referred to as glare. When the discomfort glare is caused by light sources in the field of vision, it is known as direct or discomfort glare. When glare is cause by reflection of a light source in a viewed surface, it is known as reflected glare or veiling reflection.

Your Challenge:

Measure the brightness of several surfaces in this room and calculate a luminance ratio.

Do this:

Turn the power switch to the ON position on the Minolta luminance meter and CAREFULLY take several readings along the wall surfaces and windows. Draw a quick perspective sketch and record your readings.

|  | High | Low | Ratio |
| --- | --- | --- | --- |
| Luminances of two adjacent surfaces: |
|  | Luminances of highest and lowest surfaces: |