Vital Signs EQUIPMENT DAY
Sketch Exercise No. 9

LOF: Sun Angle Calculator

(LOFSAC)

Your instrument of choice for this exercise is the Libbey Owens Ford Sun Angle Calculator. A bargain for an architect for under $20!!

Libbey Owens Ford first introduced the Sun Angle Calculators in 1951 to give architects and engineers a relatively simple method of determining solar angular values for architectural purposes. At the time it cost $5. Now, more than 45 years later the cost is only $10. Architects can once again return orienting buildings and properly controlling the sun with the emphasis on reducing air-conditioning loads and supplementing the heat source in the winter.

Your Challenge:

You will find the position of the sun at various times during the year using the LOFSAC.

Do this:

1. In the LOFSACs packet there is a Sun Chart for each four degrees of North latitude from 24( to 52. The clear wedge shaped cursor is used to read the altitude of the sun. Take a few minutes to get acquainted with: the dates -the curved lines (representing the position of the sun on the earth’s surface as seen from above); lines radiating from North represent sun time with 20 minute intervals; the tick marks at the outer edge represent the position of the sun (bearing or azimuth) from true south.

2.  Find a building with windows facing true South. Find the following information:

| Time and Date | Bearing of the Sun | Altitude of the Sun |
| --- | --- | --- |
| At 9:30 am on April 21 | 58 | 45 |
| 3:40 pm at the Equinox | 74 | 25 |
| Noon on June 21 |
| 5:00 pm on January 11 |
| Right now on this date |